Using 1-Wire™ Devices
On the
Raspberry Pi
Rusty Haddock/AE5AE
March 21, 2015

---
What is 1-Wire Technology?
A data bus
Developed by Dallas Semiconductor
(now Maxim Integrated)
Low power
Low speed
Low connector

---
What is 1-Wire Technology?
- Serial protocol - Master/slave
  - 1. Parallel port
  - 2. GPIO
  - 3. Serial Adapter (DS9097U)
  - 4. I²C Adapter (DS2482)
  - 5. USB Adapter (DS2490)
  - 6. Ethernet

---
What is 1-Wire Technology?
- Each slave device has 64-bit ID
  - 1. Factory programmed (no user prgm)
  - 2. Unique ID (custom avail.)
  - 3. Unalterable

---
What is 1-Wire Technology?
- Operates from 2.8V to 5.25V
  - 1. Power can come from 1-Wire data line
       (parasitic supply).
  - 2. Separate power line.

---
What is 1-Wire Technology?
- Packages
  - 1. TO-92 (transistor-like)
  - 2. Small IC packaging (TSOC, SOIC, SOT23).
  - 3. iButtons - 16-mm, stainless steel case.
  - 4. Generally low pin count packages,

---
Applications
- Identification only
  - PCB Id and Authentication
  - Accessory/peripheral ID
  - Access control (ID badges)
  - Asset management

---
Applications
- Control
  - GPIO bits
  - A/D conversion
- Temperature
- Time
  - 32-bit counter - 136-yr period.
  - iButton has battery & crystal built-in.

---
Applications
- NV SRAM
  - With SHA-1 crypto, used as secure token for electronic cash
  - Validation of PCB and validation of EEPROMs
- OTP (one time programmable) EPROM
  - Network address (MAC)
  - PCB ID.
- EEPROM
  - PCB ID
  - Monitor medical consumables

---
Applications
- SHA-1 secure EEPROM
  - 1. Electronic cash
  - 2. Challenge and response security.
- Logging
  - Temperature
  - Hi-res temperature
  - Passwd protection
  - Temp & humidity
  - 2- & 8-K bytes of memory

---
Applications
- 1W devices emulated by small µC
  - Text LCD Controller (Louis Swart .ZA, and others)
- DalSemi used a combination
  of switches, temperature
  sensors, and other
  miscellaneous devices to
  produce a prototype weather
  station.

---
Wiring
- Pull up
  - Data line requires a pullup resistor.
  - 4.7K ohms to +V, less if long distance or large # 1W
  - Use MOSFET for strong pullup if processor can't handle current.
- One wire
- Two wires
- Three wire

---
Wiring
- Cables
  - Gray nylon telephone cable
  - CAT-5
- Connectors
  - RJ-12 (standard)
  - Screw block

---
APIs
- Python
- C
- Perl
- TCL
- PHP
  “apt-cache search 1-wire” and see!

---
Using One Wire File System OWFS
- Easy to use, especially from shell.
  - Just use 'cat' to read.
  - Sudo apt-get install owfs owfs-doc
  - Optional web access to 1-wire devices
  - /etc/owfs.conf needs tweaking before use.
    - Comment out "server: FAKE"
    - Add FAHRENHEIT
    - Remove Localhost from "server : localhost:port = 4304

---
Using One Wire File System OWFS
- Two way to access your 1-Wire bus
  - 'sudo owfs -c /etc/owfs.conf -m /mnt/1wire -u -F''
    - Browse directories
    - Get data from device with simple 'cat'
  - 'Start owserver and companion servers
    - View 1-wire network using web browser.
    - Use 'ftp' client (?)
    <terminal session>

---
Using GPIO
- A little trickier
  - Add "dtoverlay=w1-gpio,gpiopin=4" to /boot/config.txt and reboot.
  - Wire +3.3v, GND, and GPIO4 (pin 7) todevices.
  - "sudo modprobe w1-gpio”
  - "sudo modprobe w1-therm
    <terminal session>

---
Toys
- Thermocrons (DS1921)
- LCD Display controller
- USB Master
- Reed switches and LEDs board
- DS9091K Demo & Development Kit
- TINI System

---
For More Information
- Maxim Integrated http://www.maximintegrated.com/en/app-notes
- Hobby Boards
  http://www.hobby-boards.com
- One Wire File System
  http://owfs.org
- Family Code List
  http://owfs.org/index.php?page=family-code-list
- Just Google “one wire”!